Looking at new variable to attack QCD
J. Pela

---
Strategy
- Trying to find variables combining the dijet and MET information to further suppress QCD, currently looking at:
  - Vectorial sum of Dijet and MET pT
    - Should be “zero” to events where dijet and MET are the only products from the primary interaction
  - Scalar sum of Dijet and MET
    - Should be high for signal
    - Can be used in conjunction with other variables (like with alphaT)
  - Dijet pT over Total pT (dijet+MET)
    - Should peck at 0.5 for signal
    - Very similar to alphaT can be re-written to have same behavior (sharp fall at 0.5) and can be made better with cut in HT+MET
    - Talked with alphaT people the have some data driven method to estimate QCD contamination using HT bins which we could adapt.

---
After Trigger Selection
Q CD
Scalar Sum
Dijet pT fraction
Vector Sum
VBF Inv 120

---
After Mjj>1200

---
After Delta(phi)<1.0